## Slide 1: Machine-detectors interface and Applications of particle accelerators
Nicolas Delerue
LAL (CNRS and Université de Paris-Sud)
ED PHENIICS Understanding basic principles of particle accelerators

## Slide 2: Machine detector interface

## Slide 3: How easy is it to add an experiment on an accelerator?

## Slide 4: Adding a detector in an accelerator
The detector is not transparent for the accelerator. - For example it often comes with limited apertures and a large magnet.
The accelerator will also have side effects on the detector: for example by creating backgrounds and large RF fields.
The interface between the detector and the machine need to be studied carefully.

## Slide 5: Interaction point at the ILC

## Slide 15: Beam beam effects (1)
In a collider the two beams feel each other's electric field well before and well after colliding.
Given that the particles come very close to each other, this lead to very intense forces.
These forces lead to significant disruption of the beam.

## Slide 16: Beam beam effect (2)
At the interaction point the two beams self-focus onto each other.
If the self focussing is too strong this can lead to a large emittance growth.
If the two beam are not perfectly aligned this will also lead to large transverse deflection.
This is a strong limitation on the size of the beams and therefore the luminosity, especially in a ring.

## Slide 22: Applications

## Slide 23: Quizz
Particle accelerators are not used only for HEP, they have many other applications.
In which kind of institutions are there the more particle accelerators in the world? (a) HEP lab (b) Other physical sciences labs (non HEP) (c) Museums (d) Hospitals (e) Other

## Slide 24: Answer (d)
HEP labs use the biggest particle accelerators in the world but there are only a few of them.
Non HEP physical science labs use accelerators to produce X-rays. Every large country has 1 or 2 of such accelerators (SOLEIL and ESRF in France).
Large museums like Le Louvres in Paris use particle accelerators to study cultural artefacts.
Large hospitals use particle accelerators to treat cancer => a single hospital may have several accelerators!
Most particle accelerators in the world are used for medical applications.

## Slide 25: HEP applications of accelerators
Most of the physics we are studying this week relies on particle accelerators.
The LHC is the largest of these accelerators.
Tevatron is (was) the second largest
Others include B-factories (KEKB, PEP-II), c-factories, heavy ions accelerators (BNL, GANIL, Darmstadt,…),…
Between 10 and 50 machines in the world…
To ensure maximum luminosity, a low emittance, a low beta function and a flat beam are necessary.

## Slide 26: Accelerators around Orsay
There are 29 accelerators within 10km radius of LAL. Only few of theme dedicated to HEP.

## Slide 27: Accelerators in England & Scotland
There are more than 150 accelerators.
Only 1 of them is used to teach HEP, all others are used for non HEP applications!

## Slide 28: Non HEP applications Dating old artefacts
  Radiocarbon dating is allows to measure the age of ancient artefacts.
  The ratio C13 vs C14 can be measured by using an accelerator.
  This technique is called “Accelerator Mass spectroscopy”.

## Slide 29: Accelerator Mass Spectroscopy (1)
  In an AMS device the C12, C13 and C14 beams need to be separated to allow an accurate counting.
  An energy of 10-15MV is sufficient.
  Beam stability is very important to ensure good accuracy.
  What type of source would you recommend?
  What type of accelerator? RF or electrostatic?
  Does the emittance matter?
  How would you count the charge of the ion beams with a good accuracy?

## Slide 30: Accelerator Mass Spectroscopy (2)
  AMS machines use a sputtering ion source producing C- ions.
  A tandem Van de Graff is then used to accelerate the ions and strip then to C3+.
  A DC accelerator offer a better stability than a RF accelerator.
  A Faraday cup is used to measure the beam charge.

## Slide 31: Example of AMS application Vinland map
  AMS was used to date ashes found in Newfoundland in a European-type settlement. These ashes were dated back to the XIth century.
  A viking map featuring Newfoundland was shown to be older than Columbus trip to America.
  AMS has contributed to establish that North America was visited by Vikings well before other European nations.

## Slide 32: Dating old artefacts...
  There are many other accelerator based dating techniques which I do not have time to cover.
  Proton, Neutron and light sources can all be used to investigate some properties of old artefacts.
  Left: Roman Jug dated by ISIS.

## Slide 33: Treating Cancer
  Some type of cancer tumors are located at places difficult to reach by Surgery.
  X-rays can be used to kill such tumors.
  This is called Radiotherapy.
  Radiotherapy need 10-15 MeV electrons for a few seconds.
  The accelerator needs to be compact so that it fits in an hospital room and fields can be contained.
  What type of cathode do suggest to use? Thermionic or Photocathode?
  What type of accelerators do suggest to use?

## Slide 34: Medical linac
  Radiation therapy uses small 15MeV “linacs”.
  It is safer to produce a low current over several pulses rather than a high peak current over a few pulses, hence a thermionic gun is used (such gun are also more reliable and easier to maintain).
  To reach 15 MeV with a large electrostatic accelerator would require a large installation likely to frighten the patients.
  A short RF accelerator is used to reach the required energy.

## Slide 35: Radiotherapy
  X-rays are used to kill a tumour.
  To minimize the dose sent on healthy tissues several X-ray beams are sent in turn from different directions.
  However this technique is not ideal due to its impact on healthy tissues.

## Slide 36: Proton and ion therapy
Source: Bleddyn Jones, JAI graduates lectures
What gun and what machine shall we use for proton and ion therapy?

## Slide 37: A possible solution...
Source: Bleddyn Jones, JAI graduates lectures

## Slide 38: Fast protons rings
At the moment accelerating protons in rings is slow due to resonances crossing.
R&D is ongoing to avoid that problem.

## Slide 39: Medical cyclotron
Cyclotron are well suited to accelerate ions.
Several hospitals or universities are equipped with cyclotrons to produce radioactive isotopes used as markers in drugs.
Such cyclotron is a commercial product.

## Slide 40: Pharmaceutical drugs
  To be efficient a drug need to target the correct molecule.
  This can only be achieved by studying the diffraction of intense on the molecule.
  What type of machine (gun, accelerator, ...) is best suited to deliver an intense stable beam of X-rays?

## Slide 41: A source of intense X-rays
  Synchrotrons are best suited to deliver intense beams of X-rays.
  Although synchrotrons operate at ultra low emittance the gun can be thermionic as radiation damping reduces the transverse emittance.
  A RF accelerator is then used to accelerate the particles up to the ring energy. A booster may be used to reduce the length of the linac.
Source: Diamond
Source: SOLEIL

## Slide 42: Applications of synchrotrons
  Light sources have a wide range of applications.
  A light source in England has been used to improve the quality of chocolate!
  Diamond is being used to study old manuscripts too precious to be opened!
  Protein imaging, drugs, material studies,...
  GMR (the phenomena that allows dense magnetic storage in your ipod) has been studied with light sources.

## Slide 43: The next generation of light sources
  The drawback of using radiation damping to reach ultra-low emittance is that the beam is stretched longitudinally.
  This means that the X-ray pulse have a long (ps) duration.
  Some applications require fs long high brightness X-ray pulses...
  How can this be achieved?

## Slide 44: Next generation: Linac based Free electron lasers
  Only linac based accelerators can deliver ultra-short pulses.
  Ultra-short pulses are necessary to get coherent emission of X-rays.
  Hence the emittance must be ultra-low from the start.
  This requires a photo-cathode RF gun.
  With an ultra-low emittance it is possible to achieve lasing in the undulators (and thus an even higher light output).

## Slide 45: How to make short bunches?
RF guns can be used to make short pulses.
To have even shorter pulses one needs to use a compression scheme.

## Slide 46: Neutron crystallography
  X-ray crystallography can only be used on matter that is rather transparent to X-rays.
  Other objects such as this Roman vase or the materials used to build an aircraft need a probe that penetrate deeper in the material: Neutrons.
  How can we produce neutrons?

## Slide 47: Neutrons sources
  It is not possible to directly accelerate neutrons.
  However neutrons are produced when a target is bombarded with protons.
  The ISIS neutron source requires 800 MeV protons.
  How to build this?

## Slide 48: A neutron source: ISIS
  A proton synchrotron can be used to bring the protons to the right energy.
  Emittance is not a challenge at the target location but a low emittance beam helps minimizing the losses in the accelerator (and hence the activation).
  Note that it is easier to accelerate H- than H+.

## Slide 49: Spallation
  Spallation is a process in which fragments (protons, neutrons,...) are ejected from a target atom hit by a high energy proton.
  Such target is very challenging as most of the proton power is deposited in the target.

## Slide 50: Spallation target

## Slide 51: Accelerator Driven sub-critical reactor (ADSR)‏
  An intense source of protons could be used to produce an intense flux of neutrons.
  After moderation these neutrons would trigger nuclear reactions in some nuclear material.
  Advantage the reactor can operate in sub-critical mode (if the accelerator stops the nuclear reactions die automatically).
  The nuclear fuel could be made of isotopes that can not sustain a chain reaction (such as Thorium). => no risk of proliferation.

## Slide 52: Need for high redundancy
Even if they do not like it, HEP experiments can cope with an unreliable accelerator.
In a nuclear reactor a sudden stop of the driver will cause a thermal shock.
To many thermal shocks might damage the containment vessel => The accelerator has to have a high level of reliability.

## Slide 53: ... and much more
  There are many more applications to accelerators.
  Although HEP is driving the progress other communities have now their types of accelerators.
  As new generations are built, new potentials and new possibilities are discovered.
Nicolas Delerue – University of Oxford – S19

## Slide 54: Ultra compact sources: Laser-driven plasma acceleration (1)
  An intense laser pulse shot in a plasma can accelerate electrons to very high energy: 1GeV over 33mm
  Such electron source could produce high energy low emittance electron beam over very short distances.
  This could be used to drive a compact FEL.
Leemans et al, doi:10.1038/nphys418

## Slide 55: Ultra compact sources: Laser-driven plasma acceleration (2)
  If a similar laser is shot onto a target, medium energy ions can be produced.
  This could be used for ion therapy.
+
+
+
+
+
+
+
-
-
-
-
-
-
-
+
+
+
-
-
-
-
-
CPA pulse
solid target
+
-
-
-
-
-
-
-
-
-
e-
ions
Contaminant layer
plasma sheath
Cold return
currents

## Slide 56: ThomX
ThomX is an accelerator being built at Orsay

## Slide 57: Costs
  Small accelerators can be operated by single institutions.
  Large accelerators need to be built as part of international collaborations.

## Slide 58: Progress of accelerators
Accelerators have made tremendous progress over the past 50 years.
They drove part of the developments of HEP.
However they have also become very large and expensive.

## Slide 59: Summary
Particles accelerators use principles for several fields of physics to accelerate beams of particles.
The more challenging the requirements of the users are, the more complex phenomena will appear: You can build a very crude accelerator in a University lab in a few days… but it took several years to build the LHC!
Accelerators have a wide range of applications across many scientific fields reaching all the way to archaeology…

## Slide 60: Overall summary of the lectures

## Slide 61: Particle sources & acceleration
Particles are extracted from matter either using ionisation or by creating a plasma.
There are accelerated using RF fields.
They are controlled using magnets.

## Slide 62: Basic concept (RF)
Figure of merit of EM design:
: minimize peak surface electrical field in order to reduce field emission (normalized to Eacc)
: minimize peak magnetic field to maximize achievable accelerating voltage (normalized to Eacc)
: maximize R/Q to produce more accelerating voltage Vacc for a given stored energy W in the cavity
: maximize the geometry factor to increase the cavity effectiveness of providing accelerating voltage (shape alone)
Regarding the accelerated particle and the materials (NC or SC), the optimization of RF structures will focus on these parameters

## Slide 63
Superconducting magnets is required for high energy or high current applications
    Reduction of radius of curvature and power consumption
    With room temperature magnets, the LHC circumference would be 120 km and the power consumption impossible to handle
    Bigger aperture as B  I0/aperture for dipole , I0/aperture2 for quadrupoles
    Bigger transverse acceptance
    Less beam losses, Less contraints for alignment.
WHY SUPERCONDUCTIVITY for MAGNETS ?
http://www.lhc-closer.es/1/4/6/1

## Slide 64
Superconducting RF is compulsory for CW high-current operations :
    for NC, PRF  -1/2 , for SC, PRF  
    Lower frequency  Larger longitudinal acceptance
    Larger structure  Larger transverse acceptance
          Reduced beam losses
    Energy efficiency is better : Pcryo + PRF-SC < PRF-NC
    For SC cavities PRF-SC ~ 10W (Qo ~ 5E9) @ 6.4 MV/m
    For Spoke section : PRF-SC ~ 400 kW, Pcryo ~ 600 kW
    For NC cavities PRF-NC ~ 185kW (Qo ~ 3e5) @ 6.4 MV/m
    For Spoke section : PRF-NC ~ 9 MW
    Higher accelerating gradient achievable in CW
    (in practice… not in theory) as PRF  Eacc2.
          Reduced linac length
NC = Normal conducting
SC = Superconducting
WHY SUPERCONDUCTIVITY for ACCELERATION ?
NLC, 11.4 GHz
Spoke cavity, 352 MHz
Elliptical cavity, 1.3 GHz
Quarter Wave Resonator, 88 MHz

## Slide 65
ESS Spoke Cryomodule
Vacuum vessel
Thermal shield
Cryogenic piping (supply and exhaust)
Magnetic
shield
Cavities + (focusing element)
MAIN COMPONENTS in a CRYOMODULE
Vacuum vessel
  Thermal Insulation
  Interface
Supporting components : support + alignment
MAIN COMPONENTS
Supporting components
  Supporting and positioning
Thermal shields
  Thermal Insulation
Cryogenic piping
  Cryogenic environment
Magnetic shield
  Magnetic protection
Cold mass (cavities, magnets)
Beam
Frequency tuning system
RF power coupler

## Slide 66: Dynamics & diagnostics
There are many physical phenomena that act on and in the beam.
Understanding them is important to control and improve beam quality.
Tools are necessary to be able to visualise them.

## Slide 67: Transverse Beam Dynamics : SummarY
  Charged particle in electromagnetic field :
  Cyclotron frequency : Magnetic Rigidity , Electric rigidity
  Maxwell equations : , , ,
  Maximum B achievable in iron at room temperature ~1.8T, for high B need supra !
  In bending magnet : Ampère-turn , in quadrupole :
  Quadrupole focal length :

## Slide 68: Transverse Beam Dynamics : SummarY
  General development of magnetic field around the reference trajectory:
  Beam envelop and emittance :
    Liouville theorem :
    Beam Matrix with
    Transformation :
  Field index :
  Sextupolar :
  Particles motion : Hill’s equation with
  1st order Bend Matrix (with )
  1st order Quadrupole matrix (with et ) et

## Slide 69
Longitudinal dynamics: Trajectories in the longitudinal phase space (3)
Trajectories for a 60° synchronous phase (sinus « ring-convention ») and >0
(-30° in cosinus « linac-convention »)
s =60°
Size of the bucket

## Slide 70
Longitudinal dynamics: Filamentation in longitudinal phase space
All the beam particles are thus traveling on the H = Cst curves in the (,w) space
= trajectories at frequency k0 if the forces are linear (inner bucket)
= trajectories at lower frequency when the forces become non-linear (outer bucket)
Iso-hamiltonian curves
Beam particles
The beam longitudinal rms emittance is then increasing
=> If the beam is not correctly matched to H=cte curves, filamentation is quickly observed

## Slide 71: peak performance through the years
 | 2010 | 2011 | 2012 | Nominal
bunch spacing [ns] | 150 | 50 | 50 | 25
no. of bunches | 368 | 1380 | 1380 | 2808
beta* [m] ATLAS and CMS | 3.5 | 1.0 | 0.6 | 0.55
max. bunch intensity [protons/bunch] | 1.2 x 1011 | 1.45 x 1011 | 1.7 x 1011 | 1.15 x 1011
normalized emittance [mm-mrad] | ~2.0 | ~2.4 | ~2.5 | 3.75
peak luminosity [cm-2s-1] | 2.1 x 1032 | 3.7 x 1033 | 7.7 x 1033 | 1.0 x 1034
M. Lamont, IPAC’13
>2x design when scaled to 7 TeV!

## Slide 72: And wednesday…
The first physics events of run 2 were recorded!

## Slide 73: L’installation SPIRAL2 @GANIL
The ISOL method (Isotope On-Line) to produce Rare Isotope Beams

## Slide 76: Applications of accelerators

## Slide 77: Outlook
Accelerators have a very wide range of applications both for research but also for the industry and medical treatment.
They range in size from a few meters to several kilometers.
Their operation and development requires skills from several different fields.