## Slide 1: Particle sources: Electron sources
Nicolas Delerue
IJCLab (CNRS and Université de Paris-Saclay)

## Slide 2: About me
Researcher in the Accelerator department of IJCLab.
Deputy head of the national research group (GdR) dedicated to laser-plasma acceleration.
Main research area:
  Beam diagnostics
  Laser-plasma acceleration
  Compton sources

## Slide 3: Electron sources: Content
Physical processes leading to the emission of electrons
Gun design
Beam dynamics in the gun
Diagnostics
Types of electron guns

## Slide 4: Physical process: extracting electrons
In this first part of the lecture we will see what are the conditions to be met to extract electrons from a metal.

## Slide 5: Physical process: Electrons in metal
Electrons are readily available in metals.
Eg: Copper: - 29 electrons/atom, - 9g/cm3 => 0,14mol/cm3 => 2. x1024 electrons/cm3
However theses electrons are ‘trapped’ in the metals.

## Slide 6: Electrons in metal: energy levels
In a free atom the electrons are located on orbits of increasing energy around the nucleus.
In a solids these orbits are replaced by the conduction band and the valence band.

## Slide 7: Extracting electrons from metal
The energy needed to free the electron from a solid is called “Work function”.
This work function is different for each material.

## Slide 8: Work function
The work function (W) is the minimum thermodynamic work needed to remove an electron from a solid to a point in the vacuum immediately.
E_F: Fermi energy (energy of the electrons at equilibrium).
electrostatic potential.
This depends on the configuration of the atoms on the surface so the same chemical element with different crystalline configuration will have different work function.

## Slide 9: Work function for different materials
Values of work functions are tabulated.
Source: wikipedia

## Slide 10: Quizz
Copper has a work function between 4.53 eV and 5.10 eV.
What is the wavelength of a photon with an energy of 5 eV? (a) 250 mm (b) 250 um (micrometers) (c) 250 nm (d) 250 A (Angstrom)
Reminder: c=3.108 m/s h=6x10-34J.s 1eV=1.6 10-19J

## Slide 11: Answer (c)
Copper has a work function between 4.53 eV and 5.10 eV.
What is the wavelength of a photon with an energy of 5 eV? (a) 250 mm (b) 250 um (micrometers) (c) 250 nm (d) 250 A (Angstrom)
Reminder: c=3.108 m/s h=6x10-34J.s 1eV=1.6 10-19J
As a physicist, you need at least to remember the order of magnitude a visible photon’s wavelength (2eV~620nm).

## Slide 12: Fermi-Dirac statistics
Electrons have a spin ½ so they are fermions and follow the Fermi-Dirac statistics.
Distribution (ni) of occupied states of energy (Ei) [Sommerfeld 1927]:
E_F: Fermi energy, k_B Boltzmann constant

## Slide 13: Fermi-Dirac statistics at high energy
At high energy the Fermi-Dirac statistics and the Maxwell-Boltzmann statistics tend toward the same value.
To increase the number of electron in the high energy levels you need to heat them!

## Slide 14: Extracting electrons from matter
To free the electrons you can give them more energy. - This can be done by heating => Thermionic effect - This can also be done with a laser => Photoelectric effects
Or one can reduce the work function, for example with a strong magnetic field => Schottky effect

## Slide 15: Numerical application
Copper work function: W~5eV
K_B=8.6 10-5 eV.K-1 => T~60000K
In fact this would mean that all atoms emit an electron at the same time.
To get only some atoms to emit electrons a lower temperature is acceptable.
A significant thermionic emission starts at about 2500K.

## Slide 16: Density of states for different temperatures
Source:
D.H.Dowell, USPAS

## Slide 17: Extracting electrons… Richardson’s law
We do not need all the atoms to emit electrons.
We only want a certain current.
The current density emitted (J) was studied in 1901 by Richardson.
Lambda_R: correction factor specific to a given material.

## Slide 18: Richardson’s constant
Richardson’s constant is still not completely understood.
Theoretical value : 1200mA.mm-2 K-2 but it has to be corrected for each material.
Source: http://encyclopedia2.thefreedictionary.com/Richardson's+constant

## Slide 19: Numerical application
W=5eV
A=1200A m-2 K-2
K_B=8.6 10-5 eV.K-1
Cathode area: 1 cm2 = 100 mm2

## Slide 20: Transverse energy
A hotter cathode gives a larger current.
However electrons above the emission threshold will be emitted with some kinetic energy.
Some of this kinetic energy will be converted in transverse energy.
The product of the transverse beam size by its transverse energy at a waist is called “transverse emittance”.
This will be discussed further later.
Source:
D.H.Dowell, USPAS

## Slide 21: Quizz
Let’s consider two metals with different work function.
Both metals are heated to the same temperature so that they emit electrons.
Which metal will emit the highest current? (a) Electron emission is independent from the work function. (b) The metal with the highest work function emits more electrons. (c) The metal with the lowest work function emits more electrons.

## Slide 22: Answer (c)
The metal with the lowest work function emits more electrons.
The work function express the work an electron has to do to be emitted.
The lower the work function the more electrons will be emitted (at the same temperature).

## Slide 23: Schottky emission
When a strong electric field (F) is applied the barrier for electrons to escape from the solid is lowered. => The work function is reduced.
If the field exceeds 108V/m then the electrons can also tunnel out of the solid. => Fowler-Nordheim tunneling (enhanced emission).
This effect (under the name “Edisson effect”) was used in old diode tubes.

## Slide 24: Photoelectric emission
Electrons can also receive energy by absorbing a photon.
If the energy of the photon is sufficient they will be emitted.
This is called photoelectric emission.

## Slide 25: Wavelength for photoemission
Remember: - Copper work function: 5eV - 2eV ~620nm or 5eV ~ 250nm.
The typical wavelength for photoemission is in the Ultraviolet, not in the visible.
The photoelectric effect was historically observed when a cathode was illuminated under UV light and it started to spark.

## Slide 26: Photo-electric emission
A photon incident on a material will transfer its energy to an electron present in the metal.
If the energy of this electron becomes bigger than the work function of the material, the electron can be emitted.
This is called photo-electric emission.
(image source: Masao Kuriki, ILC school)‏

## Slide 27: The 3 steps of photo-electric emission
Photo-electric emission takes place in 3 steps:
1) Absorption of a photon by an electron inside the metal. The energy transferred is proportional to the photon energy.
2) Transport of the electronto the physical surface of the metal. The electron may loose energy by scattering during this process.
3) Electron emission (if the remaining energy is above the work function; including Schottky effect)
The efficiency of this process is called “quantum efficiency”.

## Slide 28: Quantum efficiency
Not all incident photons lead to the emission of an electron.
Typical quantum efficiency is below a few percent, sometimes as low as 10-5.
As the cathode is used its surface will change and the QE will decrease.

## Slide 29: Typical cathode materials
The choice of material is a trade-off between several parameters: - quantum efficiency - environmental sensitivity - damage threshold - availability in the industry - easy handling and preparation (safety requirements)
Copper is an easy choice but with a low QE.
Cs2Te has a much higher QE but is more difficult to prepare.
Other materials: Magnesium, Niobium, GaAs:Cs
Note: GaAs:Cs can also produce polarized beams.

## Slide 30: Multiphotonic effect
Laser light conversion efficiency from IR to UV is very low and UV light transport is difficult.
Some groups have suggested that it is more efficient to illuminate a cathode with IR photons rather than converting these photons to UV: 3 IR photons can lead to the emission of an electron like an UV, however these 3 IR photons must interact with the same atom.

## Slide 31: Transverse energy
Depending on the incident photon’s energy and the travel to the surface the emitted electron will have more or less remaining kinetic energy after emission.
Once again part of this energy will be converted in transverse energy.
A higher photon energy will lead to a higher beam emittance.

## Slide 32: More exotic cathode materials

## Slide 33: Quizz
Which phenomena leads to the sparking (electron emission) when a metallic object is placed in a microwave oven? (a) Thermionic emission (because the object is heated) (b) Schottky emission (because of the electric field in the oven) (c) Photoemission (because of the photons emitted by the RF generator of the oven)

## Slide 34: Answer (b)
In a microwave oven a very intense electric field can be induced in metallic objects.
This will lead to Schottky emission (sparks).
Note: these sparks also create X-rays…

## Slide 35: Physical effects summary
Electrons are emitted when their energy exceeds the work function of the material.
3 effects can leads to this: - Thermionic emission (when the material is heated) - Schottky emission (lower emission threshold under an intense electric field) - Photoelectric emission (under illumination by energetic photons)
Material and material properties play an important role in determining the threshold and yield of these emissions.

## Slide 36: Designs of electron guns: Thermionic guns
A thermionic cathode is not sufficient to produce electrons. It must be inserted into a gun.
A thermionic gun must answer several constraints: - the cathode must be brought to a high temperature. - there must be a high electric field between the cathode and the exit of the gun (anode).

## Slide 37: Electrodes geometry (1)
Two emitted electrons repel each other.
If the anode and the cathode are flat the beam will diverge due to the charges emitted.
At low charge this effect will be small but with high current sources this will increase significantly the beam emittance.
To avoid this the shape of the electrode must compensate the space charge forces.

## Slide 38: Electrodes geometry (2)
The correct electrode shape will depend on the forces that must be compensated (ie beam current).
By solving Laplace equation it is possible to find the best shape.
(images source:Masao Kuriki, ILC school)‏
(images source: MEBS)‏

## Slide 39: Pierce gun Thermionic DC Gun
Simplest gun design.
Main features:
  Thermionic cathode
  Emission of the beam is controlled by a HV grid.
  Compensating electrode
Grid control limits pulse length. Typically >1ns.
Operated in space charge limit.
Such design is widely used.
(images source:Masao Kuriki, ILC school)‏

## Slide 40
Spring 8 SCSS thermionic gun. (images source: T. Shintake, Spring-8)‏
Example of thermionic gun

## Slide 41: The CLIO Thermoionic gun
3 stages to shape the electrons: - cathode => 1.5ns bunches - pre-buncher => 200ps - buncher => few ps
(and then the main linac structure)

## Slide 43: RF Gun
The high voltage of a DC gun can be replaced by a RF cavity.
This can provide much higher accelerating gradients and hence limit the space charge.
RF guns are often coupled with a photo-cathode.
RF gun can generate shorter bunches (and even shorter using short laser pulses).
As the RF wave is reflected on the cathode plane, a RF-gun usually has an half-integer number of cells.
(images source:Masao Kuriki, ILC school)‏

## Slide 44: Principle of a RF Photo-gun
Courtesy Jom Luiten, TUV Eindhoven

## Slide 45
Principle of a RF Photo-gun
Courtesy Jom Luiten, TUV Eindhoven

## Slide 46
Principle of a RF Photo-gun
Courtesy Jom Luiten, TUV Eindhoven

## Slide 47
Principle of a RF Photo-gun
Courtesy Jom Luiten, TUV Eindhoven

## Slide 48: Quizz
Which laser would give the best quantum efficiency on a Copper-based photo-cathode (W=5 eV)
  A 5GW CO2 laser (wavelength=10 micrometers)
  A 10 kW frequency doubled Nd:YAG laser (wavelength=532nm)
  A 3MW frequency quadrupled Ti-Sapphire laser (wavelength=200nm)

## Slide 49: Answer : (c)
QE is independent of the laser power: it is the photon energy that matters.
Remember that
The shortest the wavelength, the highest the energy. At 200nm a photon carries ~6 eV, so a 400nm photon carries ~3eV.
Note: photons with a wavelength of 532nm (2.33eV) or 10 micrometer (~0.1eV) will have less energy than the work function of the photo-cathode (but escape by tunnel effect is theoretically possible).

## Slide 50: RF photocathode gun

## Slide 51: Power amplification: Klystron
A klystron amplifies a milliwatt RF signal to kilowatts or megawatts so that it can be used in RF accelerating cavities.

## Slide 53: PHIN RF Gun

## Slide 54: Field line simulations (SUPERFISH)

## Slide 69: Cavity shape
The cavity shape has an impact on the peak field.
A higher peak field may lead to more breakdowns and limit the maximum acceleration gradient.

## Slide 70: Higher order modes
In addition to the TM010 mode of the cavity, higher order mode may be excited.
These higher order mode can cause longitudinal and transverse instabilities.
Special filters are used to remove them.

## Slide 72: Quizz
The RF gun built at LAL have a frequency of 2998MHz.
What is the length of a full cell? (a) 5cm (b) 50cm (c) 5m

## Slide 73: Answer (a)
One cell is half a wavelength.
At 3GHz one wavelength is about 10 cm.
(c/2998MHz)/2 ~5cm

## Slide 74: Examples of quantum efficiencies: SLAC-TN-05-080
Source: D.T. Palmer, SLAC-tn-05-080

## Slide 75: Quantum efficiency: DESY XFEL (EPAC’04 MOPKF021)
Material Cs2Te (very high QE)

## Slide 76
Source: USPAS 2008

## Slide 77: Photocathode preparation and lifetime

## Slide 79: Laser technology
Lasers can’t produce UV light (˜ 260nm; ˜5 eV) directly.
The most efficient lasers emit in the near infra-red. For example Ti:Saphire [Ti:Al2O3] (800nm;1.5eV) or Nd:YAG (1064nm;1.2eV).
Non linear crystals are then used to triple or quadruple the energy of the photons.
Such laser systems (and frequency conversion) are rather complex and need special skills to operate.
See your laser courses for more about this…

## Slide 83: Dark current
Electrons can also be emitted at time when they are not wanted: - when the grid is “closed” in a thermionic gun - when there is no laser light in a photogun.
This is called “dark current”.
Dark current particles are often at the wrong phase and therefore at the wrong energy.
The dark current is a source noise and must be removed.
Source: http://journals.aps.org/prstab/abstract/10.1103/PhysRevSTAB.17.043401

## Slide 85: RF gun vs Thermoionic injector
In a Thermoionic injector the electrons are bunched in several stages.
In the RF gun the electrons immediately reach the desired pulse length (down to ps). => Better compactness => Lower emittance
BUT: more complexity (laser, RF,…)

## Slide 86: Summary: Gun design
The shape of the electrodes is important in all electron guns: - it will minimize space-charge - it will allow to increase the field without breakdowns
Cavity shape are important in RF guns to increase even further the accelerating field.

## Slide 87: Beam dynamics in the GUN

## Slide 88: Beam dynamics: Space-charge effect
Let's consider two particles with similar charges travelling in the same direction.
Due to their charge these particles will push each other away (Coulomb's law).
What is the intensity of the force with which they repel each other?
What is the effect of a full bunch?

## Slide 89: Coulomb force between two electrons
Assume d=1micrometre.
f=2 10-16N
This may look small but an electron is not very heavy
f/m=2.5 1014N/kg
This force is very intense on the scale of the electrons.
Typical charge in a bunch: ~100pC = 6 108 electrons

## Slide 90
Avoiding space-charge effects
If there is a second force that cancels the effect of the space-charge the particle will not be deviated.
Let's see how the shape of this electrode is defined...

## Slide 91: Electrostatic potential in the beam
Assume steady state
Particle conservation as they propagate => Current constant across gap
Electrostatic potential is 0 at source hence, particles are accelerated in the gap.
Hence, by substitution
And thus
(see also Humphries, CPB, sec 5.2)

## Slide 92: Electrode design
Electrostatic potential in the beam: Laplace equation:
Trial function:
Hence the potential
Hence for the source electrode:
And for the extraction electrode:

## Slide 93: ... and then?
After the anode space charge effects are still present.
It is not possible to use an electrostatic solution anymore.
The compensating field must have a circular symmetry...
This is not easy to achieve!

## Slide 94: Compensating solenoid (1)
The solution is to use a compensating solenoid.
Inside the solenoid the field is so that the angular momentum of the particles couples with the field.
BUT at the edge of the solenoid the particles decouple from the field and receive a transverse kick (Busch theorem).

## Slide 95: Busch theorem
Canonical angular momentum must be conserved.
In a solenoid charged particles couple their transverse momentum to the field.
At the edge of the solenoid the field suddenly decreases.
To conserve the correct coupling the particles will be deflected toward more intense field (ie the middle of the solenoid)
This will induce a focussing effect.

## Slide 96: Compensating solenoid (2)
To achieve the best compensation effect, several small solenoids are much better than a big one (as this maximizes the edge effect).
This can be seen on this picture of the Diamond gun.
Once high energies are reached the particles travel fast enough so that the space charge do not need to be compensated any more.

## Slide 97: Quiz
On this image of the CLIC injector the electrons travel from the left to the right.
In which direction does the current flow in the solenoid to compensate the space-charge effect?
a) Clockwise
b) Counter clockwise
c) It does not matter

## Slide 98: Answer: a
Busch theorem:
To get a negative transverse kick the second term must be positive.
q is negative.
So the flux must be positive.
The electrons must travel in the direction of the flux.
The current must circulate in a clockwise direction.

## Slide 99: Space-charge limitation
Emitted electrons shield the cathode from the anode => reduced field
This limits the intensity of the emission. Child-Landmuir law (potential Vd, area S, distance d) [This is more complex when the field is not constant]
(images source:Masao Kuriki, ILC school)‏

## Slide 100: Space charge limited emission
In the case of a photo-injector the space charge with limit the intensity that can be extracted from the cathode.
The charge extracted from the cathode will also depend on the shape of the laser pulse.

## Slide 101
BSA= Laser beam diameter

## Slide 102: Quizz:
(a) Because of space-charge.
(b) Higher laser energy will induce more heating in the cathode and reduce the QE.
(c) There is a trade off between laser energy and RF power.
Why the relation between laser energy and charge is not linear?

## Slide 103: Answer (a)
(a) Because of space-charge.
(b) Higher laser energy will induce more heating in the cathode and reduce the QE.
(c) There is a trade off between laser energy and RF power.
Why the relation between laser energy and charge is not linear?

## Slide 105: Quick introduction to emittance
Remember the perfect gas law: PV=nRT
This is a statistical law that is also valid for particle bunch.
V is the volume term (x*y*z)
P is the pressure term, it corresponds to the kinetic energy of the particles in each plane (x’*y’*z’).
n and R are proportionality terms (R is unit dependent and could be 1 with the correct choice of units).
T is called the temperature for gas… For a particle beam it is called “emittance”.
You can split the emittance into longitudinal emittance (along z or s) and transverse emittance (along x and y).

## Slide 106: Space charge and emittance
Space charge will lead to an increased emittance => lower beam quality.

## Slide 107: Emittance compensation
By calculating how the different slices of the beam will propagate in the gun on can minimise the emittance at the exit of the gun.

## Slide 108: Transverse dynamics in the gun
The emission from the cathode lasts a finite time.
During that time the RF phase varies.
Hence the head and the tail of the bunch will experience slightly different acceleration.

## Slide 109: Longitudinal dynamics in the gun: velocity bunching
After the cathode the electrons are not yet relativistic.
Electrons with more energy will go faster.
Depending on the phase at which the particles will be produced, the bunch at the exit of the gun can be longer, shorter or have the same length than the initial laser pulse.

## Slide 110: Summary for beam dynamics
The electrons emitted by the gun interact with each other.
This must be taken into account when trying to optimise the gun.
Space-charge is one of the dominating effect, but the different phases at which the particles are generated must also be taken into account.
All these effects, once understood, can be simulated and, sometimes, mitigated.

## Slide 111: Gun conditionning
The gun must be conditionned to accept the full RF power.
During conditionning small impurities and surface defect are burnt out.

## Slide 112: History

## Slide 114: Examples and classification of injectors

## Slide 115: PHIL: Photo injector at LAL: Overall layout

## Slide 116: PHIL: Photo injector at LAL: The accelerator

## Slide 117: PHIL: Photo injector at LAL: The Gun

## Slide 118: Quizz
What do you need to build a photoinjector? List the main components…

## Slide 119: To build a photo injector you need:

## Slide 120: Summary
3 effects can be used (or combined) to produce electrons: thermionic, schottky and photoelectric.
Careful design is necessary to reach high electric field.
To reach the best beam for the application one also need to take into account the dynamic of the particles in the gun (and after).
There is a large variety of electron gun (current, emittance, rep. rate,… ) suited to different applications.

## Slide 121: Recommended readings (and credits for some of the material used in this lecture)
USPAS course on particle sources D.H.Dowell et al.
USPAS Course on High Brightness electron injectors, 2007
An Engineering guide to Photoinjectors, T. Rao and D.H.Dowell